## Slide 1: EMV Solutions
SLIM CD, INC

## Slide 2: EMV Liability Shift - What changed?
Counterfeit Cards - Stolen card data burned onto mag stripe of a different card
Merchant
Keyed transactions at register
All Card Not Present transactions
(phone, ecommerce, mobile)
Cardholder’s Issuing Bank
Swiped transactions (in person)
Merchant
Swiped transactions (in person)
Keyed transactions at register
All Card Not Present transactions
(phone, ecommerce, mobile)
Cardholder’s Issuing Bank
EMV Chip Transactions
Until Oct 2015
After Oct 2015

## Slide 3: EMV - Fully Integrated
Touches EMV data
Touches Cardholder Data
Full feature-functionality controlled by ECR/POS
In scope for EMV
In scope for PCI (may be reduced by P2PE)

## Slide 4: EMV – Partially Integrated
POS software touches EMV data
POS software touches Cardholder Data
Feature-functionality controlled by POS software
Out of scope for EMV
May be in our out of scope for PCI

## Slide 5: EMV – Semi Integrated
Only PINPAD touches EMV data
Only PINPAD touches Cardholder Data
Functionality controlled by PINPAD
Out of scope for EMV
ECR out of scope for PCI

## Slide 6: EMV in the cloud
PINPAD with VPN IP
POS SYSTEM
SLIM CD

## Slide 7: Option 1 - Direct Web Service Payment Calls
SlimCD.com
Payment
Web Services
POS or Kiosk Stack
1. POS Interface Code
2. Developer integrates to device
3. SlimCD Web Services or libraries
4. Device Driver from Device Company
POS Interface Code written by the POS developer.
Developer contacts device directly, with full control over all prompts and transaction flow.
Developer uses SLIM CD Web Services or libraries to process through Vantiv (or others)
Hardware manufacturer provides Windows device drivers (if needed)
The developer touches the cardholder data
EMV and PCI certification by the developer IS REQUIRED

## Slide 8: Option 2 -.NET Libraries on a POS or Kiosk
POS or Kiosk Stack
1. POS Interface Code
2. SlimCD Hardware Abstraction Layer
3. SlimCD Per-Device Code
4. Device Driver from Device Company
POS Interface Code written by the POS developer.
SlimCD Hardware Abstraction Layer is a set of calls that allow the developer to call the same methods for:
  Connecting
  Starting a transaction by sending an amount (etc.)
  Getting back the approved/declined results
SlimCD Per Device Code communicates with the device and to SLIMCD.COM
Hardware manufacturer provides Windows device drivers (if needed)
SlimCD.com
Payment
Web Services
The developer never touches the cardholder data
No EMV certification required by the developer

## Slide 9: Option 3 -VPN on a POS, with Web Services
SlimCD.com
Payment
Web Services
POS, WEB or Kiosk Stack
1. POS Interface Code
POS Interface Code written by the POS developer.
Developer calls web service on SLIM CD’s side that handles all communication with the driver.
Web Services return approved/declined as XML.
The developer never touches the cardholder data
No EMV or PCI certification required by the developer
SAQ-B can be used by merchant because device is part of our VPN network
SlimCD.com
Hardware Web Services
2. SlimCD Hardware Abstraction Layer
3. SlimCD Per-Device Code
4. Device Driver from Device Company

## Slide 10: Option 4 –Launch Our App
POS Stack
1. POS Interface Code
2a. SlimCD Hardware Abstraction Layer
2b. SlimCD Per-Device Code
4. Device Driver from Device Company
POS Interface Code written by the POS developer.
Launch the SLIM CD app, providing amount and transtype in an XML file
SlimCD for PC operates the hardware and writes back a response
SlimCD.com
Payment
Web Services
The developer never touches the cardholder data
No EMV or PCI certification required by the developer
2. SlimCD for PC

## Slide 11
Leveraging Existing Products
PC
Mobile
Web

## Slide 12: TransClient – Slim CD Desktop Software
Runs transactions
Supports SEARCH
Supports clerks/users
Prints Receipts
Captures Signatures
Sends email receipts
Credit, Debit, Check, Gift
Retail, Restaurant, Hotel, etc
CAN BE LAUNCHED by other apps

## Slide 13: TransClient Supports New Pinpads TODAY!
VX 805
MX 915

## Slide 14: SlimCD for PC – The new desktop app
Works like TransClient.exe
  MSR readers
  Keyed transactions
  Plus - EMV PINPads!!
SLIM CD web-managed client/clerk logins (like the website and mobile devices)
XML Login and REQ file support

## Slide 15: EMVDLL - Pinpads
VX 805
MX 915
IPP320
ISC250
VERIFONE
INGENICO

## Slide 16: Launched App Demo
Uses XMLLogin.XML
Uses standard XML.REQ and XML.ANS files
Supports additional data for Hotels in the XML
Support for Hotel Prompts is coming in V2
Support for checks and gift cards is coming in V2
Product in extended BETA now.

## Slide 17: VB and.NET versions of “Launcher app
Supports
  TransClient
  SlimCDForPC

## Slide 18: Mobile – EMV devices
Apple/IOS, Google/Android, Microsoft/WinPhone
Supports swiped and keyed today.
Support for IDTECH EMV Headset Jack in development
IDTECH’s new contact/contactless device coming
Support for IDTECH BTPay Pinpad (Bluetooth with PIN capability)
“Launch Our App” functionality still available.
Microsoft Win8/Win10 Tablets will be supported

## Slide 19
Unified API
PC
Mobile
Web

## Slide 20: Slim CD Libraries & Web Services
http://developer.slimcd.com
http://www.slimcd.com/developers/downloads
Using the Library:
ProcessTransactionRequest req ;
ProcessTransactionReply reply ;
Launching our App:
LaunchTransactionConfig cfg ;
LaunchTransactionRequest req ;
LaunchTransactionReply reply ;

## Slide 21: SLIM CD for EMV – Hardware Abstraction
function int Hardware.Initialize (ConfigFile,callback)
function Hardware.GetCapabilities()
function Hardware.ProcessTransaction (config, request)
function Hardware.CloseConnection()

## Slide 22: New .NET version of “Launcher app
Identifies the differences
New tab to create the XMLLOGON
(Available later today?)
Supports
  TransClient
  SlimCDForPC

## Slide 23: Demo Hardware Sample
Sample code for this tab
on the following page.

## Slide 25: Receipt Information

## Slide 26: Pass Through Command

## Slide 27: WebService
http:/testdevice.slimcd.com/devices.asmx
Accepts JSON in name/value pairs:
connect= { json for a DeviceConnectRequest }
cfg= { json for a DeviceTransactConfig }
req= { json for a DeviceTransactRequest }
Returns XML of the data (Will also return JSON soon)

## Slide 28: WebService
Standard .NET webservice
Connects:
TCP/IP
MAC
UDP
Can Identify device by MAC or Serial#

## Slide 29: DeviceTransactionReply from WebService

## Slide 30: Suggested Tools from the manufacturers
You WILL want/need to play with these devices and get to know them!
VeriFone
  Drivers for 32 and 64 bit
  vFHostTerm allows command testing
  MXDownloader – update OS, XPI, etc
  DDL.EXE - Used for downloads
  FormManager
Ingenico
  RBA Drivers and kits
  RBA Test Application
  LLT.EXE - Used for downloads
  Ingenico Telium Forms Tool

## Slide 31: Slim CD Libraries & Web Services
New websites
http://developer.slimcd.com
http://www.slimcd.com/developers/downloads
EMV Developer’s Kit RESOURCES page
http://test.slimcd.com/EMV

## Slide 32
EMV Configuration

## Slide 33: Supporting Merchants
Ordering Hardware
  Prices change with inventory levels
  Always “get a quote”
  The internet has better pricing, but for the wrong thing
Correct cabling
  USB is not “USB” as we know it.
Some assembly required
  Bring a small screwdriver for VX assembly
Additional parts (and more parts)
  Power supplies
  Ethernet/USB cables
  I/O Blocks

## Slide 34: Google Search for Pinpads or Cables
Lots of “knock offs”
Lots are contact-only
Prices are misleading
Most Internet deals require getting a merchant account from the seller.

## Slide 35: VeriFone VX Cables to use
USB: CBL282-038-01-A
Last digit 01, 02, or 03
(1=1m long, 2=3m long, 3=1.8m long)
Ethernet: CBL-282-006-01
PWR-282-001-01
BLOCK with USB: CBL-282-044-01
PWR-282-001-01

## Slide 36: VeriFone VX Cables – Contact/Contactless
The “head” of the cable can have 1 set of pins or 2 sets of pins. You need BOTH sets to do CONTACTLESS.
CONTACT-ONLY
CONTACT AND CONTACTLESS

## Slide 37: VeriFone MX Cables to use
VeriFone says the built-in ports will cause you grief.
I/O Module – You need one for the cables
    P132-602-00-R (Red, with extra ports)
    P132-601-00-R (No extra ports)
Cables are color-coded and fit into I/O module
  USB Cable: 23741-02-R (BLUE)
  TCP/IP CABLE: 24173-02 (PURPLE). This IS AN EXPENSIVE CABLE!
Power Supply: PWR132-003-01-A (FOR A CABLE!)

## Slide 38: Ingenico Cables
Same cables for IPP or ISC devices
Same connection for USB, Serial or TCP/IP
Power supply needed on ALL cables

## Slide 39: Ingenico connectors are the same

## Slide 40: Code signing
Whoever downloads the first “signed” package into a VeriFone “owns” the device in VeriFone’s eyes. If you buy one one EBAY, you may NOT be able to configure and use it!
Code is signed by VeriFone. Slim CD has it’s own signing keys at VeriFone. VeriFone also uses their own DEV signing key.\
Removing an old signature requires either sending back to VeriFone or getting a special file from them per serial number. This will WIPE EVERYTHING, including PIN DEBIT keys.
Ingenico signs their products, but differently. It can be updated afterwards.

## Slide 41: Remote Key Management
PIN DEBIT or MSR keys
Done by downloading a “signed package” from VeriFone or Ingenico.
This means THEY MUST HAVE the key.
They both have SLIM CD’s keys, but they MAY NOT have the PIN DEBIT keys for everyone.

## Slide 42: CAPK
Certificate of Authority Public Keys
Issued by each “brand”
There are “test” and “production” values. You need the right one in the right situation.
Downloaded anytime, and MUST be maintained as the card brands update the keys.
Processors are starting to “deliver” keys when batches close
Merchants have 6 months from the expiration of a key to get it off the device.
https://www.eftlab.co.uk/index.php/site-map/knowledge-base/243-ca-public-keys

## Slide 43: Estate Management
Tracking devices by serial number (we now send Device Serial Number and other data PER TRANSACTION)
Inventorying the software version of devices in the field. All must be kept in sync with gateway updates. NOT AN OPTION.
Updating CAPK keys
Pushing new patches as they are released
  And certified? - Does the change require a recert?
  PCI?
  New firmware?
  New Kernel? (DOES require recertification)

## Slide 44: Estate Management Options
The device does NOT need to be connected to the internet. The software that manages the device does.
VeriFone and Ingenico offer these products
ISOs and processors may or may not include you in their offering (they DO have this for terminals already, they just are not eager to use it for PINPADS… Don’t know why, other than the effort to do it)
SLIM CD will have a solution that works with it’s systems and coordinates with it’s payment gateway releases.

## Slide 45: EMV Devices - Costs in time and effort
Procuring proper devices
Assembling the hardware
Loading the firmware
Inventory management and tracking
Updating and maintenance
Configuring for merchant-specific desires (credit, debit, etc)
Understanding the data requested and the impact
  Floor Limits
  TAC values, Terminal Capabilities settings, VISATTQ, etc
  https://www.eftlab.com.au/index.php/site-map/our-articles/161-the-use-of-ctqs-and-ttqs-in-nfc-transactions

## Slide 46: Contact and Contactless
These are so similar, but are two different “worlds”.
Ingenico has separate XML configuration files for each
Data can fall back to CONTACT settings when doing contactless, but not the other way
There are different “limits” and constraints
There is a different “transaction flow” for contactless
Effects cabling, software configuration, and terminal options.

## Slide 47: Processor Scheduling
We are working with 3 processors to start:
  Vantiv - Have finished message testing. They made changes since we last ran, so they asked us to re-run some contactless tests (should be done next week)
  TSYS has an issue with their own DEBIT keys and are issuing new test key. Once available, we will finish the last 6 messaging transactions with them
  First Data North – Recoding for Restaurant & Hotel in progress so we can support EMV on NORTH (we previously only did Retail on North, because that’s all that needed PIN DEBIT before EMV changed everything)
Other processors will be done next year
  Global
  Elavon
  Chase/Paymentech
  RBS WorldPay

## Slide 48: Estate Management & Configuration
Database Designed
Local Version
Microsoft Azure “Cloud” version
Internal Maintenance Tools
MS-Access
Web
Device-Specific Data
Verifone 75% complete
Ingenico ready for data entry
IDTECH (Mobile/BTPay) starting

## Slide 49: Internal tool for data entry
Hierarchical Data
Schema - Card Brand
RID Data – Card Plan
AID Data – Card Specifics
CAPK – Public Keys
Terminal Data
Caps – Device Capabilities
TAC – Terminal Action Codes
Available features/prompts, etc
Processor Data
Supported AIDs
Required DDOL
Floor & other limits
Merchant Data
Cards – Credit/Debit, etc
Floor Limts & options

## Slide 50: PinPad Configuration

## Slide 51: VeriFone: Generate D-Commands

## Slide 52: Sample Output
<?xml version="1.0" encoding="UTF-8"?>
<SlimCDTerminalConfigForVerifone>
<Commands>
<LINE_0000 type="DCommand">4431323030</LINE_0000>
<LINE_0001 type="DCommand">4431363031303038</LINE_0001>
<LINE_0002 type="DCommand">44313500783000000000005649534100000000000000000000 … 00000</LINE_0002>
<LINE_0003 type="DCommand">44313500783000000000004D61737465724361726400000000 … 00000</LINE_0003>
....
<LINE_0278 type="DCommand">443137002F30303041303030303030363230303632300000000 … 303030</LINE_0278>
<0279 type="Reboot"></0279></Commands>
<Control>
<TerminalOwner>Vantiv Test Device</TerminalOwner>
<TerminalMake>VeriFone</TerminalMake>
<TerminalModel>VeriFone</TerminalModel>
<TestOrProduction></TestOrProduction><TerminalSerialNumber>12345</TerminalSerialNumber>
<ProcessorName>Vantiv</ProcessorName>
<CommandCount>280</CommandCount>
</Control>
</SlimCDTerminalConfigForVerifone>

## Slide 53: Alternative Configurations
Each option requires a new certification (per device, per processor)
We can turn off a certified option WITHOUT having to re-certify
Some MCC codes require independent certification
Kiosk, unattended, and other configurations are considered separate certifications
Feel free to review EMV BOOK 4 and the VeriFone/Ingenico letters and let us know if you need a different certification.

## Slide 54
EMV Considerations

## Slide 55: EMV - EMV Kernels expire!

## Slide 56: EMV Certifications Expire
Contact good for 3 years
Contactless good for 2 years
CONTACT CERT – 3 Years | CONTACT CERT – 3 Years
CONTACTLESS CERT 2 yrs | CONTACTLESS CERT 2 yrs | CONTACTLESS CERT 2 yrs

## Slide 57: EMV Certifications - Timeline
Contact good for 3 years
Contactless good for 2 years
YEAR 1 | YEAR 2 | YEAR 3 | YEAR 4 | YEAR 5 | YEAR 6
CONTACT CERT | CONTACT CERT
CONTACTLESS CERT | CONTACTLESS CERT | CONTACTLESS CERT
 |  | cless resert | cont resert | cless resert | 
There is a 2 year use from the certifications.
THEN recertify for each of the next 3 years
Then skip a year and start again.

## Slide 58: SLIM CD Responsibilities
SlimCD is your Payment Gateway and PC Software Provider.
  Avoid EMV Certifications
  Reduce PCI Risks
  Provide an Omni-Channel suite of software products that touch cardholder data and accept transactions
We provide assistance with the payment within our software
Most merchant services providers and POS vendors wish to use their existing hardware vendors and keep costs for customers to a minimum. We agree. Use your preferred vendors to install the hardware and associated drivers, etc.

## Slide 59: Hardware Ordering Details
Hardware Distributors install the default values for a device, based on the order
  Operating System
  Applications
  PIN Keys
  Data/MSR Encryption keys (P2P)
Devices will need to be injected with PIN Debit keys by an authorized injection facility (wherever you do it today). The merchant account provider’s keys will need to be used. Contact that provider to identify which facility injects keys on their behalf.
Distributors can request “bundles” that contain a standard SLIM CD configuration for VeriFone software so that it can be used out of the box. Ingenico can already be used out of the box and needs no such bundle
  VeriFone MX devices – Use XPI 5200P, signed by SLIM CD
  VeriFone VX devices – Use XPI 8.4.3, signed by SLIM CD
  Ingenico devices – Use RBA 16.02

## Slide 60: Connectivity Options
USB/Serial – Available today
USB/HID – An Ingenico option, available today
TCP/IP – Available on Ingenico, coming soon to VeriFone
  VeriFone considerations
    Static IP –vs- DHCP
    Find device by MAC
    SSL on or off
    Proxy Server
    PassPhrase / Client Auth / Server (See vHostTerm for these options)

## Slide 61: Customer “Look & Feel”
Once we certify an OS with an XPI or RBA, it MUST remain that way
Custom forms can be used without needing certification
VeriFone
  FormAgent forms can be downloaded outside of XPI and can be done at any time
  XPI Packages WILL need to be signed (offline discussion for those that want to provide custom logo or branding for their customers)
Ingenico
  Custom forms can be downloaded outside of RBA updates without being signed.

## Slide 62: Additional Opportunities
We recommend that the hardware reseller deliver the hardware and install the drivers on the PC, configure the hardware (if needed) then test it for proper operation.
Some maintenance will need to be performed to the devices as the CAPK keys are expired/retired in 2017.
For those that wish to be “hands off” and have carte-blanche services, SLIM CD can assume the responsibilities for PC driver installation, hardware configuration, ongoing device maintenance etc. Stay tuned for more information on this option, including a schedule of fees and referral income options for this service.

## Slide 63: Q & A
Getting help from VeriFone and Ingenico is difficult at this time.
Questions on EMV… Send emails to: frank@slimcd.com